## Slide 1: CSC Sparks Analysis
Iurii Bordulev, Aleksandr Khodinov, Sergei Rosliakov

## Slide 2: The Task
Stand by period = low current
Stable beam period = high current
What to find: Current sparks in Stable beam periods

## Slide 3: Implementation
Step 1: Analyze the current data
Step 2:
Define the threshold (for stable beam)
Choose region above threshold
Step 3:
Define the Stable beam region
Fit the baseline
Define the threshold (for sparks)
Detect the spark

## Slide 4: Implementation
Step 2. The threshold (for Stable Beam region)
The data for HV are used
When the HV is nominal, I count the avg current
The avg. current + threshold value (defined by user) = Threshold for Stable Beams

## Slide 5: Implementation
Voltages
Step 2. The threshold (for Stable Beam region)

## Slide 6: Implementation
Step 3. Define the Stable beam region
Fight with regular current falls in 2018 data

## Slide 7: Implementation
Step 3. Fit the baseline
With exponent

## Slide 8: Implementation
Step 3. Define the threshold (for sparks) above the baseline
Higher the baseline value –> higher the baseline oscillations –> the threshold should be higher not to detect the oscillations.
When the run is long (> 5 hours) – the baseline oscillations in the middle of the run is also lower –> the threshold could be smaller to detect smaller sparks
The dynamic threshold were introduced (dependent on the baseline value and the length of the run) = 1 – 2 microAmps

## Slide 9: Implementation
Step 3. Define the threshold (for sparks) above the baseline

## Slide 10: Implementation
Step 3. Detect the spark
Parameters of sparks:
Chamber; layer; time stamp; Amp; Bline; Timediff; HV

## Slide 11: Algorithm
CRON
Part I
Python scrip
Download data
Currents; HV
Process the data
Add entry to database
Database
Remove data
Repeat for every layer
Part II. When all layers processed
C++ script
Analyze database
Make a root tree
Root Tree
Launches everyday at 00:00
Location: @aiatlas066.cern.ch:/data/software/python3/baranov/sparkcounter

## Slide 12: Root tree
[seconds since Jan 01 1970]
[microAmps above baseline]
[microAmps]
[seconds]
[1-4]
Positive – A side; Negative – C side
[ppm]
[Volts]

## Slide 13: Changed parameters
Humidity
HV

## Slide 14: HV

## Slide 15: Chambers and layers (Statistics)

## Slide 16: Amplitude Distribution at different Humidity

## Slide 17: HV

## Slide 18: Amplitude distribution with different HV

## Slide 19: Timediff distribution at different Humidity

## Slide 20: Timediff distribution at different HV

## Slide 21: Count rate VS HV
How it looks like

## Slide 22: Timediff VS Amplitude

## Slide 23: Baseline

## Slide 24: Amplitude VS Baseline

## Slide 25: Timediff VS Baseline

## Slide 26: Conclusion
Humidity increase:
don’t change the form of Amplitude distribution of the sparks;
leads to decrease of the sparks rate.
HV increase:
shortens the amplitude distribution of the sparks and make it more homogeneous;
significantly increases the sparks rate.
Baseline (Luminosity) increase:
doesn’t change the Amplitude distribution;
increases the sparks rate.

## Slide 27: Thank you for your attention